Summary of Revisions to Wetland Mapping Standard

as a result of Public Review Comments

Clarifications to Objectives and Scope, including:

  - Reference to OMB Circular A-16 (revised)

  - Use of ancillary data is supported, just not a requirement

  - Clearer language and organization for Exemptions section

  - Addition of Exemption for Marine and Estuarine benthic habitat mapping - currently necessitated by the use of different definitions & classifications

  - Addition of Exemption by Waiver: In order to ensure the best available data can always be included…

Waiver Process

- A waiver is an authorized exemption from a specific minimum requirement in the standard

- An exemption may be granted based on data quality, but not on cost

- The waiver allows for comprehensive coverage of “best available” data more quickly, meeting the needs of many end users

- The U.S. Fish and Wildlife Service data steward for water resources and wetlands is the final authority for the waiver process

Revisions to Technical Requirements:

  - “In-shore Deepwater” language was changed throughout the document to specify “Estuarine and Lacustrine Deepwater”

  - Clarified what is meant by Source versus Base Imagery, and their respective requirements, added glossary definition for imagery

  - Clarified Classification Level requirements - Special Modifiers only required “where applicable”, other details in footnotes updated

  - Clarified that the Target Mapping Unit measure allows for mapping below a specified threshold, but does not subject that finer detailed mapping to the accuracy requirements of the standard

  - Clarified that Producer's Accuracy is measured by both Feature and Attribute accuracy

  - Feature accuracy is the correctness of the identification of wetland vs. non-wetland

  - Attribute accuracy is the correctness of the classification of the wetlands using the FGDC Wetlands Classification Standard

- Additional requirement added for Attribute accuracy: must be at least 85%

- Datum and Projection clarified

  - Wetlands data may be created or used in any standard datum and projection

  - However, data must be re-projected to Albers Equal-Area projection and NAD83 (or higher) prior to NSDI submission

- FWS Coordination and Quality Control:

  - Mapping entities are advised to consult with FWS to coordinate (to assure a logical, technically sound, and comprehensive approach)

  - FWS will be responsible for final quality control of all products

Revisions to Appendices:

- Appendices were classified as Normative or Informative

- Most Informative appendices have been removed from the final standard since they were included to inform public comment

- The removed Informative appendices will be used to shape the Implementation guidelines (under development)

- The final version contains 3 appendices:

  - A: Attributes for Wetland Classification (Normative)

  - B: Attributes for LLWW (for Landscape, Landform, 	Water Flow path, and Waterbody Type (Informative)

  - C:  Definitions (Informative)

- Better quality graphics are provided for Attributes for Wetland Classification (Normative)

- Definition section has been updated to reflect the other revisions to the standard